$ git clone http://review.coreboot.org/coreboot.git
$ cd coreboot/util/ectool
$ make
$ sudo make install

The proprietary BIOS of Thinkpad laptops include an interface called SMAPI which allows setting these thresholds, and other cool things. Unfortunately, coreboot doesn’t include this. If you’re an X200 user you might be in luck as the patch for supporting tpacpi-bat is currently in code review.
For us there’s a workaround too, though not as clean. We can manually control the RAM of the embedded controller, the chip that handles the battery and charging, and many other things. For that you need ectool, which is included in coreboot’s git repository, in coreboot/util/ectool. Simply use make to compile it.

X200/X200s uses the same smapi port as xx20 models, but the way BIOS talk to EC is different in these machines.
Now I can switch between different settings to save my battery.
sudo ectool -w 0x3 -z 0x44 && sudo ectool -w 0x24 -z 0xd0 && sudo ectool -w 0x3 -z 0x40 && sudo ectool -w 0x24 -z 0xb2 for saving the battery and
sudo ectool -w 0x3 -z 0x44 && sudo ectool -w 0x24 -z 0xd7 && sudo ectool -w 0x3 -z 0x40 && sudo ectool -w 0x24 -z 0xd7 to make a almost full charge.

sudo ectool -w 0x3 -z 0x44 && sudo ectool -w 0x24 -z 0xb2 && sudo ectool -w 0x3 -z 0x40 && sudo ectool -w 0x24 -z 0xa8
ESTE ES 40%-50% (CREO QUE SERIA MEJOR CAMBIARLO A 45%-50%) CAMBIAO ABAJO

sudo ectool -w 0x3 -z 0x44 && sudo ectool -w 0x24 -z 0xb2 && sudo ectool -w 0x3 -z 0x40 && sudo ectool -w 0x24 -z 0xad

FULL CHARGE 95%

sudo ectool -w 0x3 -z 0x44 && sudo ectool -w 0x24 -z 0xdf && sudo ectool -w 0x3 -z 0x40 && sudo ectool -w 0x24 -z 0xad

While we’re at it, here’s a table containing the values to write to byte 0x24 for different percentages:
Percentage	0x24 value
10	0x8a
15	0x8f
20	0x94
25	0x99
30	0x9e
35	0xa3
40	0xa8
45	0xad
50	0xb2
55	0xb7
60	0xbc
65	0xc1
70	0xc6
75	0xcb
80	0xd0
85	0xd5
90	0xda
95	0xdf
100	0xe4

Byte 0x03 allows for configuring if we’re setting the start or stop threshold. Specifically, bit 2 (=4) of byte 0x03. If we’re setting the stop thresholds (percentage at which the battery should stop charging), we set this bit to true:
# ectool -w 0x3 -z 0x44
We can then specify the threshold. Simply note the percentage you’ll like, and set bit 7 to true, by adding 128. 80% becomes:
80+128 = 208 = 0xD0
Set this threshold by writing it to byte 0x24 of the EC’s RAM:
# ectool -w 0x24 -z 0xD0
For setting the start threshold (percentage at which the battery should start charging), do the same but set bit 2 of byte 0x03 to false:
# ectool -w 0x3 -z 0x40
# ectool -w 0x24 -z 0xB2
This sets the start threshold to 50%.
I currently run this in a script that runs at boot. It’s not required though, since the EC will remain active when the battery is plugged in and has charge, even when the laptop is “off”.